## Slide 1: Secure Cloud Manufacturing
Routing Plan
Fall 2017

## Slide 2: Assembly and individual parts
Part 2 - Cabin
Part 1 - Chassis
Part 3 - Trunk
Wheels

## Slide 3: Testbed floor plan
M
V
LEGEND
M - Mechanical gripper
C - Vacuum gripper

## Slide 4: Parts and process numbers
Process # | Part 1 - Chassis | Part 2 - Cabin | Part 3 - Trunk
0 | Raw material | Raw material | Raw material
1 | Machined top (CNC1 – Vacuum) | Machined bottom (CNC2 – Mechanical) | Machined bottom (CNC2 – Mechanical)
2 | N/A | Inspected | Inspected
3 | N/A | Flipped | Flipped
4 | N/A | Machined top (CNC3) | Machined top (CNC4)
5 | Inspected (finished) | Inspected (finished) | Inspected (finished)

## Slide 5: Flow diagram
Assign Part # at RFID 6
Machined in CNC 2
Machined in CNC 1
Update to process 3 at RFID 1
Machined in CNC 3/4
Update to process 1 at RFID 1
Inspection at Camera 1
Update to process 5 at RFID 2
Inspection at Camera 1
Update to process 2 at RFID 2
Inspection at Camera 2
Update to process 1 at RFID 1
Flip part in Cell 1
Update to process 4 at RFID 3
Update to process 5 at RFID 4
Start
End
Read part/process # at RFID 1/3
Part 1
Part 2/3

## Slide 6: Machining: Part 1 - Chassis
Process #1: top surface face milling
  Vacuum gripper to CNC 1
  Tool: ¼” end mill
  Process: 1) 0.25mm Facing 2) 0.2” deep passes Area Milling
  Time: 1 + 20 minutes
Post processing: wheel holes drilling
  Manual
  Tool: ¼” drill
  Process: 4 x 0.5” holes
  Time: 4 x 2 minutes
0.79”
(120mm)
2”
(50.8mm)
3”
(76.2mm)
0.5”
0.2”
Process #
0 | Raw material
1 | Machined top
2 | N/A
3 | N/A
4 | N/A
5 | Inspected (finished)

## Slide 7: Machining: Part 2 - Cabin
Process #1: bottom surface pocketing
  Mechanical gripper to CNC 2
  Tool: 1/8” end mill
  Process: 5mm deep rectangular cut
  Time: 1 minute
Process #4: top surface stepped face milling
  CNC 3
  Tool: 5/16” drill
  Process: 1/8” deep passes
  Time: 20 minutes
Process #
0 | Raw material
1 | Machined bottom
2 | Inspected
3 | Flipped
4 | Machined top
5 | Inspected (finished)
2”
1.5”
2”
1.5”

## Slide 8: Machining: Part 3 - Trunk
Process #1: bottom surface pocketing
  Mechanical gripper to CNC 2
  Tool: 5/16” end mill
  Process: 5mm deep rectangular cut
  Time: 1 minute
Process #4: top surface pocketing
  CNC 4
  Tool: ¼” drill
  Process: 12mm deep rectangular cut
  Time: 20 minutes
Process #
0 | Raw material
1 | Machined bottom
2 | Inspected
3 | Flipped
4 | Machined top
5 | Inspected (finished)
2”
1.5”
2”
1”
1.5”
12mm