## Slide 1: PLC Training Fall 2017
Christopher Shu (Mechanical subteam) shuchris@umich.edu
Gibin Joe Zachariah (Controls subteam) gibinzac@umich.edu

## Slide 2: Outline
Introductions
  Chris Shu: CNC part centering
  Gibin Zachariah: Camera
Introduction to PLCs (from other training presentations)
  Background
  Hardware and testbed
  Software and ladder logic
  Example
  Testbed

## Slide 3: CNC Part Centering
Goal was to design a method of holding different sized workpieces accounting for robot placement inaccuracies
Previous method centered part to undefined origin, secured it by two line contacts, and didn’t work for thicker workpieces
New design centers to known vise origin, secures by surface contact, and is adjustable for different sized workpieces

## Slide 4: Camera
Used for quality control.
Defects are identified through image processing and are sent out without doing further processes.
Increases efficiency and reduces wastage of machine time.

## Slide 7: PLCs: Background
Programmable Logic Controllers (PLCs) were developed due to the need of reconfiguration in automotive manufacturing, which relied on wiring and relay-based control systems
PLCs are used in the automotive, petroleum, and chemical industry, CNC manufacturing, others
There are many brands of PLCs. They are programmed with languages standardized in IEC 61131-3. One of those languages is ladder logic.
Automation control system diagram:
Input Sensors
Output Actuators
Process
Programmable Logic
Controller
Measurement
Resultant
Actions
Notes: International Electrotechnical Commission.

## Slide 8: PLCs: Hardware and testbed
CPU: Main control center that evaluates the logic and changes outputs every 5 to 50 ms
Power supply: Supplies power for the CPU and I/O sections
Programming interface device: Computer used to write a ladder program that can download (send to PLC), upload (read from PLC) or go online, and has a monitor. Studio 5000 is the application software for programming the PLCs we use
I/O modules: Work with voltages higher than the CPU can handle. These modules “isolate” the PLC and protect its circuits.
Power supply
Slot [0] : CPU
Slots [1:n] : I/O section

## Slide 9: PLCs: Hardware and testbed
Example diagram of a manufacturing plant
Inputs:
Limit switches
Proximity
RFID sensors
Processor
Input/Output
Modules
PLC
Conveyor
Pick-up
point
CNC
drill
Parts
bin
Robot
arm
Process
Outputs:
Motors
Solenoids
Pneumatic actuators
Programming Terminal
Notes: HARDWARE: “Loops” (conveyors), “Cells” (cages for robots), “Hold Stops?” (pallet stoppers), “Diverter” (between conveyors, directing pallet flow), CNCs, Cameras, RFID sensors, RF modules

## Slide 10: Software and ladder logic
We use Studio 5000® Logix Designer from Rockwell
Ladder logic is the first/most popular PLC programming language (functional block is another)
The Ladder Diagram (LD) programming language originated from the graphical representation used to design an electrical control system
  Control decisions were made using relays
  After a while relays were replaced by logic circuits
  Logic gates used to make control decisions
  Finally, CPUs replaced logic circuits
  Relay Logic representation (or LD) developed to make program creation and maintenance easier (control decisions accomplished through programming)
  Computer based graphical representation of wiring diagrams that was easy to understand
  Reduced training and support cost
CPU

## Slide 11: Software and ladder logic
A rung of ladder diagram code can contain input and output instructions
  Input contacts serve as conditional statements for executing output coils (commands)
Ladder logic execution
  Rungs of ladder diagram are solved from left to right and top to bottom
  Branches within rungs are solved top left to bottom right
Timers and counters are other operations used to delay operations

## Slide 12: Additional references
See shared network drive for references
  Video by Ziyan Zhang F16 (61mins):
    02_MDP > 03_Control > Training Materials > PLC Training.mp4
    02_MDP > 03_Control > Training Materials > PLC Basic Training.pptx
  PPT on ladder logic basics
    02_MDP > 02_Mechanical > Winter 2017 > Training_2017 > PLC Training > PLC Programming.pptx
  PPT on ladder logic by Rockwell Automation
    02_MDP > 02_Mechanical > Winter 2017 > Training_2017 > PLC Training > PLC Ladder Diagram.pptx
  PDF compilation of all material by Chris Shu and Adrian Pinto W17:
    02_MDP > 02_Mechanical > Winter 2017 > Training_2017 > PLC Training > Compilation of PLC Training Material and Examples.pdf

## Slide 13: Example
Introduction to PLCs and Ladder Logic concepts: relay-based circuit example and ladder logic origins